## Slide 1
BASIC ELECTRICAL AND ELECTRONICS ENGINEERING
Course Code: CSE1002
Mrunmayee Rahate
Assistant Professor, DYPIU
SCHOOL OF COMPUTER SCIENCE ENGINEERING AND APPLICATIONS

## Slide 2
Module 2: Semiconductor Devices and Applications
Lecture 1: Introduction to Semiconductors

## Slide 4
Semiconductor Material
Notes: Number of electrons in shell is equal to .
For most atoms (in Groups 1–18 of the periodic table), stability is achieved when the outermost shell has 8 electrons — this is called the octet rule.
A full shell (8 valence electrons) makes the atom very stable but nonconductive — because there are no free electrons to move.
Conductor: Most conductors have few valence electrons that are loosely bound and can move freely.
Ex: Gold (Au), Silver (Ag), Copper (Cu)) have only 1 valence electron
Number of electrons in 𝒏^(𝒕𝒉 )shell is equal to 〖𝟐𝒏〗^𝟐.
For most atoms (in Groups 1–18 of the periodic table), stability is achieved when the outermost shell has 8 electrons — this is called the octet rule.
A full shell (8 valence electrons) makes the atom very stable but nonconductive — because there are no free electrons to move.
Conductor: Most conductors have few valence electrons that are loosely bound and can move freely.
Ex: Gold (Au), Silver (Ag), Copper (Cu)) have only 1 valence electron

## Slide 7: Types of Semiconductor

## Slide 8: Intrinsic Semiconductor (At Kelvin)
At low temperatures (near absolute zero), semiconductors act like insulators because all electrons are in the valence band
Stable Crystalline Structure

## Slide 9
As a semiconductor is heated, thermal agitation gives electrons enough energy to jump from the valence band to the conduction band
Creates electron-hole pairs in a crystalline structure
Increase in temperature increases the number of free charge carriers (both electrons and holes)
Intrinsic Semiconductor (At Room Temperature)

## Slide 10
Free electrons are being generated continuously while some recombine with holes
Conductivity of a semiconductor material increases with the temperature
Intrinsic Semiconductor (At Room Temperature)

## Slide 11
Extrinsic Semiconductor
A large surplus of negative charge carriers are created, making the material much more conductive than it was in its pure, intrinsic state
Notes: The number of dopant atoms in a semiconductor varies based on the desired electrical conductivity and is typically in a range that is much smaller than the host semiconductor atoms. Low doping levels are around one dopant atom per or host atoms, while high doping levels are on the order of one dopant atom per host atoms.
The number of dopant atoms in a semiconductor varies based on the desired electrical conductivity and is typically in a range that is much smaller than the host semiconductor atoms. Low doping levels are around one dopant atom per 10^8 or 10^7 host atoms, while high doping levels are on the order of one dopant atom per 10^4 host atoms.

## Slide 12: n-Type Material
■
Each pentavalent atom (antimony, in this case) forms covalent bonds with four adjacent silicon atoms
Four of the antimony atom’s valence electrons are used to form the covalent bonds with silicon atoms, leaving one extra electron
This extra electron becomes a conduction electron because it is not involved in bonding
Because the pentavalent atom gives up an electron, it is often called a donor atom
The number of conduction electrons can be carefully controlled by the number of impurity atoms added to the silicon
A conduction electron created by this doping process does not leave a hole in the valence band because it is in excess of the number required to fill the valence band
Extrinsic Semiconductor

## Slide 13
Extrinsic Semiconductor
A large surplus of holes are created, making the material much more conductive than it was in its pure, intrinsic state

## Slide 14: p-Type Material
■
Each trivalent atom (Boron, in this case) forms covalent bonds with four adjacent silicon atoms
Three of the Boron atom’s valence electrons are used to form the covalent bonds with silicon atoms, leaving one extra hole
Because the trivalent atom can take up an electron, it is often called an acceptor atom
The number of holes can be carefully controlled by the number of impurity atoms added to the silicon
A hole created by this doping process is not accompanied by a conduction (free) electron
Extrinsic Semiconductor

## Slide 15
Majority and Minority Carriers
Majority charge carriers are due to thermal agitation + doping
Minority charge carriers are due to thermal agitation only

## Slide 16
Thank You !!!